## Slide 1: Path Planning
George Slagley

## Slide 2: The Movement Problem
We know the area(arena layout)
Walls/ghosts act as obstacles for the roboi
Move in an efficient manner so no time is wasted

## Slide 3: What is Path Planning?
Also known as motion planning
It is essentially a problem where an object has to move from point a to point b
  In practice, this is usually in the most efficient way, while avoiding “Forbidden Regions”

## Slide 4: The Dimensions of the Problem
Our project entails a full 3-dimensional workspace
  We have a point in a plane (x,y), this can be easily represented by an 2d array
  BUT we also have an optional rotation θ
  So the full parameters we are able to work with is (x,y,θ)

## Slide 5: Important Base Concepts for Path Planning
Configuration Space:
  Effectively, you reduce the robot to a single point for ease of calculations and then you scale the environment accordingly(Shown in pictures on the next slide)
Free Space:
  This is the space where the robot can traverse, no issues
Target Space:
  This is the endpoint, the goal
Obstacle Space:
  Robot Cannot move to these
  HOWEVER this is not simply the compliment of the free space, because the free space also includes target space/configuration space/scaled space

## Slide 6: Picture For Spaces
Configuration Space for a point sized robot:
Configuration Space for a rectangular robot:

## Slide 7: Ways to Traverse these spaces
Grid Based: Best for low dimension problems, easy to program. Effectivity lay a grid on the workspace and use it as a coordinate system
Geometric: Uses “Visibility” techniques to determine if the robot is going to collide with something(effectively calculates some vectors from point a and b and picks the path with the smallest magnitudes without collision)
Interval: weird
There are more, but they are extremely complicated and require lots of computation/math that is unnecessary for our situation

## Slide 8: Storage
The arena map should be stored in a 2d array(unscaled or scaled?)
The possible paths need to be stored in trees, this is the best way I’ve seen
  Leads to tree traversing algorithms to find the shortest paths
  Trees data should store (x,y) possibly θ, “heuristic cost”, moving cost, parent/child node
  changes based on algorithm

## Slide 9: First Notable Algorithm: Dijkstra's
Shortest path zoom zoom

## Slide 10: Second Notable Algorithm A*
Works with incentive values to move
  Calculates the movement cost, which is the immediate cost of moving to the next square
  Then calculates a estimated moving cost in relation to goal (heuristic cost)
  Adds them together to get a total cost, and then move to the place with the lowest cost
If the algorithm doesn’t calculate estimated moving cost, then it defaults to Dijkstra's algorithm

## Slide 11: Third Notable Algorithm: Rapidly-Exploring Random Tree(RRT)
It literally just spams trees till it hits the destination, and then just drives to it
  It’s visualization is anxiety inducing
  Super inefficient/random….but neat

## Slide 12: Links
https://www.geeksforgeeks.org/binary-tree-data-structure/
https://www.geeksforgeeks.org/a-search-algorithm/
https://en.wikipedia.org/wiki/A*_search_algorithm
https://en.wikipedia.org/wiki/Motion_planning
http://correll.cs.colorado.edu/?p=965
https://en.wikipedia.org/wiki/Rapidly-exploring_random_tree